## Slide 1: Interchange Design
Nick Hoernke, Bill Roth and Eric Sorensen

## Slide 2: Presentation Overview
Interchange Characteristics
Process for Interchange Type Selection
Service Interchange
System Interchange
New Type of Interchange
Design Process and Details
Interchange Attributes to Consider

## Slide 3: Interchange Characteristics
Two main types of interchanges
      Service Interchange – between a freeway or controlled access facility and a lower class roadway such as an arterial or collector (i.e. diamond)
      System Interchange – between two or more freeways or controlled access facilities (i.e. cloverleaf)

## Slide 4: Interchange Characteristics
Attributes of interchange type varies
      Traffic Operations
      Safety
      Physical Impacts (R/W)
      Construction Cost
      Constructability

## Slide 5: Process for Interchange Type Selection
Process for Interchange type selection
      Data Collection
      Planning Framework
      Identify and develop Concepts
      Evaluate and Screen Alternatives
      Select Preferred Alternative

## Slide 6: Process for Interchange Type Selection
Additional items to consider
      Identify and understand key project issues
      Design creativity and context sensitivity
      required to develop feasible solutions
      Maintain fiscal feasibility
      Maintain/enhance local access in reconstructing urban system ramp interchanges
      Incorporating exclusive HOV lanes or ramps
      Complicates the design and increases cost
      Constructability
      Reconstruction typically requires maintaining all movements

## Slide 7: Service Interchange
Urban and Suburban Areas (tight R/W constraints)
      Single Point Design creativity and context sensitivity
      One intersection vs. two along local roadway
      Expensive
      Compressed or Tight Diamond
      Intersections spaced 250’-400’ apart
      Similar footprint to SPDI
      Operational Characteristics
      Determine number of lanes
      Traffic operations are key to success

## Slide 8: Service Interchange
Single Point Diamond Interchange (SPDI)

## Slide 9: Service Interchange
Urban and Suburban Areas (tight R/W constraints)
      Single Point Design creativity and context sensitivity
      One intersection vs. two along local roadway
      Expensive
      Compressed or Tight Diamond
      Intersections spaced 250’-400’ apart
      Similar footprint to SPDI
      Operational Characteristics
      Determine number of lanes
      Traffic operations are key to success

## Slide 10: Service Interchange
Compressed or Tight Diamond Interchange

## Slide 11: Service Interchange
Urban and Suburban Areas (tight R/W constraints)
      Implement selection process
      12 points for the design of system interchanges
      Maintain route continuity
      Maintain basic number of lanes
      Provide lane balance and continuity
      Maintain appropriate ramp spacing
      Design ramps for freeway speeds
      Select appropriate interchange types
      Employ only right-hand entrances and exits
      Provide single exit at interchanges
      Provide exits in advance of crossroad
      Provide decision sight distance in advance of exits
      Eliminate weaving within interchanges along the mainline
      Provide designs that can be simply signed

## Slide 12: New Type of Interchange
Diverging Diamond

## Slide 13: Design Process and Details
Stakeholders
      Maintaining Authority
      Traveling Public
      Impacted Public
      Landowners
      Environment
      Politics
      Federal Funding
      Be Honest!

## Slide 14: Design Process and Details
Geometrics
      Iterative process
      Provide desirables
        DSD, SSD, etc…
      Avoid flat spots and crown transitions
      Rollovers
      Nearby interchanges
      Lane Balance
      Barrier Concept
      Adequate Signing
      Structures - Construction restrictions to traffic

## Slide 15: Design Process and Details
Traffic
      Large trucks
      Avoid off-ramp queueing onto freeway
      Analysis for staging and permanent conditions.
Milwaukee area – Congestion map

## Slide 16: Design Process and Details
Staging
      Finding the optimal balance
      Impacts of staging
        Tie-ins & project length, ROW, Utilities
        Justify expenditure to provide desirable features
      Over the top first
      Traffic considerations
        Seasonal peaks
        Concurrent projects along corridor

## Slide 17: Design Process and Details
Staging continued…
      Structures
        Lateral and vertical clearance
        Construction joints
        Future fill/cut at footings
      Settlement of embankments
      Design drainage for winter maintenance
      Early project to eliminate complications
      Lessons learned

## Slide 18: Interchange Attributes to Consider
Design
      Type, Size:
      Single point, trumpet, three leg, one quadrant, diamond, cloverleaf, etc…
      Based on typically 6 warrants
      Determine # lanes, heavy movements, crash locations.

## Slide 19: Interchange Attributes to Consider
Design Continued…
      Utilities
        Existing? Proposed?
      Space or R/W constraints
      Real Estate
      Safety, Safety, Safety
      AASHTO Green Book, FDM, AASHTO RDG, MUTCD. How do these affect the design?

## Slide 20: Interchange Attributes to Consider
Users
      Local Facilities
      Economics
      Travel Times
      Utilities - NIMBY
      Multi-modal
      Environmental/Recreation

## Slide 21: Future Considerations
Future Considerations
      Additional Lanes / Interchange capacity
      Future development in the immediate area
      Overhead utilities and constructability of structures
      OSHA requirement for cranes
      Address in utility coordination
      Temporary traffic shifts for maintenance and rehab
      Leave in crossovers used for construction
      Wider, “beefed up” shoulders necessary?

## Slide 22: Future Considerations
Future Considerations Continued…
      Profile gradient should be steep enough to accommodate future barrier wall when highway expanded.
      Ramp Metering
      Ramp spacing between terminals
      Congestion
      Queue spillback
      Stop and Go travels
      Heavy weaving
      Poor traffic signal progression

## Slide 23: Questions????